DVB-S/S2 Digital TV

Quick Install Guide

- Getting Started

The product is fully compatible for your desktop PC use. Enables you to enjoy digital Radio and TV programs.

1.1 Feature

*DVB-S/S2 TV and radio program receiving on PC

*Real-time and Pre-Scheduled Recording (PVR)

*Time-Shifting

*HDTV support (MPEG2)

*DVB Electronic Program Guide (EPG)

*Transponder / satellite auto scan

*Teletext

*Subtitles

*DiSEqC 1.0/1.1/1.2 support

*Full screen display

*On screen display

*Remote control supported

*DVB core based plug in supported

  - System Requirements

Recommended Platform:

- *2.0 GHz CPU or above

- *256 MB RAM (required), 512 MB RAM (recommended)

- *Sound card for audio / onboard sound chip

- *One free USB2.0 port (USB model)

- *CD-ROM / DVD-ROM (For driver & application installation)

- *Windows XP Service Pack2 / Vista

- *Microsoft Direct X 9.0 or above

1.3 Package Includes

*Digital TV PCI Card / USB Box

*Remote Control (With batteries)

*USB cable (For USB model)

*IR receiver cable (For PCI model)

*Power adapter (For USB model)

*Quick Installation Guide

*Software CD (Driver and Application Software)

2. Connections

2.1 Hardware Insatllation

- USB model:

- *Connect the signal cable(from LNB) & DC power to your digital TV product

- *Connect USB Cable to the USB port on your PC

PCI model:

- *Plug into PCI slot on your PC (turn off your PC beforehand)

*Plug in the signal cable & IR receiver cable to your digital TV card

- Driver and Software Installation

Step1:

When you insert PCI or connect USB Digital TV product to your PC.

“Found New Hardware Wizard” dialog will pop out; choose ”No,,not this time” and click ”Next”.

Step2:

Insert Software CD into CD or DVD drive.

On following dialog, choose ”install from a list or specific location (Advanced)” and click “Next”

Step3:

On following dialog, choose ”Search for the best driver in these locations”, tick “Search removable  media (floppy, CD-ROM…)” and click “Next”.

Step4:

If following dialog appears, click “Continue Anyway”.

Step5:

In following dialog, click “Finish”, then Hardware installation is completed.

Step6:

Insert the Drive CD into your CD-ROM, .TeVii Installshell will automatically start & follow window will appear. If the window doesn’t appear, start TeVii Installshell from Drive CD manually. Click on

“Install myTeVii”.

Step7:

Installation process starts; press “Next” button on each installation step.

Step8:

After installation finished, you will see myTeVii icon on your Desktop. Run it by double clicking the icon. Then you will see the name of your DVB card shown on the bottom of splash-screen.

If you see “OFFLINE” on the screen, it means your card hasn’t been recognized by your PC.

Make sure you plug card into PCI/USB slot firmly and installed driver again.

Step9:

After splash-screen, you will see main window of application.

Click on video area (at the first run it will look like large black area) by right mouse button.

Pop-up menu appears. Follow menu: Settings ->LNB/DiSEqC settings & Scan…

Step10:

LNB/Transponders settings. you will see settings for satellites and transponders.

1) Find and click on required satellite on list. Fill appropriate LOF1, LOF2, SW values. Please  read instruction of LNB convertor you use. If you see universal (dual-band) Ku LNBF then usual parameters are: LOF1=10600000, LOF2=9750000, SW=11700000. If you use DiSEqC switch or motor then click on DiSEqC button and choose appropriate LNB input port (see next picture).

Don’t forget to click on “Apply” button when you finish setup satellite LNB parameters.

2) Click on button “Sel All” (right side of window) to select all transponders or while holding “Ctrl” key click sequentially on every transponder you want to scan. Click on button “-=SCAN=-“ to start scanning process.

Step11:

DiSEqC Switch Settings. Mark “First DiSEqC Switch” and choose Committed, LNB1..LNB4 (depend on required port of switch)

Step12:

Scan Dialog:

You can watch scanning process in this window. You may interrupt scanning by clicking “stop” button. After scanning completed, close scanning window and then LNB dialog.

Step13:

Open pop-up menu by clicking right mouse button on main window, then follow steps below:

Display -> Video On/Off. Make sure there is a mark sign on this option. If there is no such mark then click on it.

Step14:

Click on any channel name with green “V” sign. You may organize channel view by clicking on any of following buttons “Sat”, “Prov”, NetID”, “Transp”, “Fav”, “All”

Three small buttons “All”, “V”, “R” can filter channels to show TV only, Radio only or all channels.

Note: you may press second and third time on the same button to filter channels and show free-to-air only (green), encrypted only (red) or all (yellow)

# Text boxes

Digital TV Tuner #1

The model name of hardware shown here